## Slide 1
Porting EVR to AMD Xilinx Zynq Ultrascale+
Timing Workshop
EPICS Collaboration Meeting
Rutherford Appleton Laboratory
April 11, 2025

## Slide 2
AMD Xilinx Zynq Ultrascale+
PS (Processing System)
  Powerful MPSoC
  Dedicated I/O pins
  Runs independently of PL
  Peripherals include GigE, PCIe, I2C, etc.
  Runs Linux
PL (Programmable Logic)
  FPGA
  AXI connectivity to PS
  High-Speed GTH transceivers

## Slide 3
AMD Xilinx Zynq Ultrascale+ Booting Process
FSBL (First Stage Boot Loader)
  Initialization
  Boot device initialization
  Partition loading
  Handoff
U-Boot
Linux
FPGA Configuration in Linux
Documentation somewhat hard to find and digest

## Slide 4
AMD Xilinx Zynq Ultrascale+ in Vivado
Block diagram
Not version control friendly
Portability across Vivado versions
Extract Block Design
  TCL script to regenerate block design

## Slide 5
AMD Xilinx Zynq Ultrascale+
IP core generator
.xci files text based but not version control friendly nor portable across Vivado versions
Extract TCL from log file

## Slide 6
Version Control for FPGA source code
HDL (VHDL/Verilog)
Instantiation in HDL
TCL scripts for IP cores
TCL scripts for project setup and implementation
Constraints in human readable text files
No block designs/GUI tools needed

## Slide 7
IOxOS IFC_1414
Zynq Ultrascale+ mTCA.4 Processor AMC
Single VITA 57.1 FMC slot
SFP+ slots in front panel
Class D1.2 RTM interface
Si5341B clock generator
  Reference clock for EVR
LMK04616ZCR clock cleaner for system clocks
  Cannot be used for EVR clock cleaning

## Slide 8
Xilinx KR260 Robotics Stater Kit
Lots of I/O
SFP cage for transceiver
Two fixed GTH reference clocks
  156.25 MHz and 74.25 MHz

## Slide 9
Xilinx KRIA K26 SOM
General Specifications
Dimensions (with heat spreader)
  77 mm x 60 mm x 11 mm
Application Processor
  Quad-core Arm® Cortex®-A53 MPCore™ up to 1.5 GHz
Real-Time Processor
  Dual-core Arm Cortex-R5F MPCore up to 600 MHz
Graphics Processing Unit
  Mali™-400 MP2 up to 667 MHz
Video Codec Unit (VCU)
  1 - up to 32 streams (total resolution ≤ 4Kp60)
Trusted Platform Module (TPM)
  Infineon 2.0
Memory On-Chip*
  26.6 Mb On-Chip SRAM
Memory On-SOM
  4GB 64-bit DDR4 (non-ECC) and 16 GB eMMC
High-Speed PS Connectivity (GTR)
  PCIe® Gen2 x4, 2x USB3.0, SATA 3.1, DisplayPort™, 4x Tri-mode Gigabit Ethernet
General PS Connectivity (MIO)
  2xUSB 2.0, 2x SD/SDIO, 2x UART, 2x CAN 2.0B, 2x I2C, 2x SPI, 4x 32b GPIO
GTH 12.5 Gb/s Transceivers
  4 (PCIe Gen3 x4, SLVS-EC, HDMI 2.0, DisplayPort 1.4)
GTR 6 Gb/s Transceivers
  4
PS MIO (1.8V)
  49
PL High-density (HD) I/O (3.3V)
  69
PL High-performance (HP) I/O (1.8V)
  116
System Logic Cells (K)
  256
DSP Slices
  1,248
Typical Power
  7.5W

## Slide 10
VHDL Board top level
Top level HDL (PL)
  I/O pins
  GTH reference clocks
  GTH RX/TX pins
I2C and other I/O goes through PS
  PS pins not present in PL design

## Slide 11
psi_common_axi_pkg
Part of psi_common library to enhance readability and unifying code through all files
psi_common_axi_pkg provides record types that groups AXI signals and keeps interconnections tidy
https://github.com/paulscherrerinstitute/psi_common

## Slide 12
Linux PL_CLK issues
Recent Linux versions turn off unused clock coming from PS to PL side
Not an issue on Linux shipped with IFC_1414
2022.1 PetaLinux Starter Kit pre-built SD card image for KV260, KR260 seems to work

## Slide 13
Linux Tools for Ultrascale+
I2C
  i2cdetect -y -a -r 1 for listing device on I2C bus 1
  i2cset -y 1 0x71 0x20 for writing 0x20 to device 0x71 on bus 1
  i2cset -y 1 0x76 0x06 0xbf for writing 0xbf to address 0x06 on device 0x76 on bus 1
  i2cdump -y 1 0x75 dump 256 registers on device 0x75 on bus 1
devmem
  devmem 0xa8000000 read 32 bit value at memory address 0xa800000
  devmem 0xa8000008 32 0x00000047 write 32 bit value to address 0xa8000000

## Slide 14
Current Status of Ultrascale+ EVR Port
Started working in IFC_1414 but switched over to KR260
  Did not have FMC module for I/O
  IFC_1414 is missing scope probing points
  IFC_1414 has one green/red PL controlled LED in front panel
    Additional LEDs on PCB but difficult to see in crate
  KR260 has
    PMOD connectors for probing/additional LEDs
    Two fixed reference clocks for EVR
EVR visible from Linux through AXI (devmem)
Link is up, EVM shows round-trip delay
HW outputs on KR260 PMOD working
Delay compensation is not working
Missing clock cleaner

## Slide 15
Licensing
Will be released open source
Software license MIT, BSD?

## Slide 16
Acknowledgements
Till Straumann for his work on the CPSI_CIO Zynq Ultrascale+ port of the EVM for SLS-II
  Example of using TCL scripts for generating IP cores instead of using .xci files
  Introduction to the PSI AXI wrappers