## Slide 1
MRF latest developments
Timing Workshop
EPICS Collaboration Meeting
CEA Saclay
April 23, 2026

## Slide 2
cPCI-FOUT-12 / VME-FOUT-12
Due to requests a new batch of cPCI-FOUT-12 / VME-FOUT-12 Fan-Outs for 230 Series Hardware was produced
Available now
Micro-Research Finland Oy

## Slide 3
mTCA-EVR-300GTX
New product coming up (first batch May 2026)
Similar to mTCA-EVR-300U (in photo)
  Both Universal I/O slots driven by two GTX outputs, four GTX outputs in total
  GTX outputs support fine tuning delay with 1/2560 event clock resolution (~3 ps @ 125 MHz)
Micro-Research Finland Oy

## Slide 4
Firmware Changes
Micro-Research Finland Oy
New EVM features
Added port specific shutters for the upstream ports separately for both events and DBUS bits (version 13)
New EVR features
Fast Event bypassing Delay Compensation FIFO (version 24)
Support of fine delays for VME-EVR-300 GTX outputs, delay adjustable with 1/2560 event clock cycle precision (~3 ps @ 125 MHz event clock) (will be available from version 12250207)

## Slide 5
VME SAM3X Microcontroller Firmware
Micro-Research Finland Oy
By Sebastian Marsching (KIT)
Applies to VME-EVM-300 and VME-EVR-300
Improved UDP support
  32 bit read/write operations
  Improved reliability and speed
Added support for JTAG XVC Server (remote FPGA firmware upgrade over ethernet)
Upgrading of FPGA firmware required:
  VME-EVR-300 version 12260207 (not yet released)
  VME-EVM-300 version 22140207 (not yet released)

## Slide 6
Fast Event – Delay Compensation
Micro-Research Finland Oy
EVM
EVM
EVM
EVR
EVR
EVR
EVR
50 m
75 m
80 m
150 m
30 m
50 m
Target delay 1 μs (~200 m)
DC FIFO delay 350 ns
DC FIFO delay 250 ns
DC FIFO delay 475 ns
DC FIFO delay 375 ns
*) This example does not take EVM/EVR internal latencies into account

## Slide 7
Fast Event – Operating Modes
Micro-Research Finland Oy
Fast Event Disabled
  All events go through DC FIFO
Fast Event Enabled – High Priority Fast Event
  Fast event processed immediately after reception, bypasses DC FIFO
  All other events go through DC FIFO and can be delayed by one cycle
  Risk of losing event in case there is more than one fast event and a continuous train of other events
Fast Event Enabled – Low priority Fast Event
  Fast event gets processed as fast as possible waiting for empty event slot from events from the DC FIFO
  Timing of non-fast events is not altered

## Slide 8
Fast Event – Normal Mode
Micro-Research Finland Oy
RX
DC FIFO
Fast Event
detection
1 Event
buffer
Mapping RAM

## Slide 9
Fast Event – Fast Event Mode
Fast Event detected, no event from DC FIFO
Micro-Research Finland Oy
RX
DC FIFO
Fast Event
detection
N/A
1 Event
buffer
Mapping RAM

## Slide 10
Fast Event – Fast Event High Priority Mode
Fast Event detected, simultaneous event from DC FIFO
Micro-Research Finland Oy
RX
DC FIFO
Fast Event
detection
XX
1 Event
buffer
Mapping RAM

## Slide 11
Fast Event – Fast Event High Priority Mode
Fast Event processed, events from DC FIFO delayed
Micro-Research Finland Oy
RX
DC FIFO
Fast Event
detection
XX
1 Event
buffer
Mapping RAM

## Slide 12
Fast Event – Fast Event High Priority Mode
Return to normal mode after gap from events from DC FIFO
Micro-Research Finland Oy
RX
DC FIFO
Fast Event
detection
1 Event
buffer
Mapping RAM

## Slide 13
Fast Event – Fast Event Low Priority Mode
Fast Event and simultaneous events from DC FIFO
Micro-Research Finland Oy
RX
DC FIFO
Fast Event
detection
Fast
1 Event
buffer
Mapping RAM

## Slide 14
Fast Event – Fast Event Low Priority Mode
Fast event processed in gap from events from DC FIFO
Micro-Research Finland Oy
RX
DC FIFO
Fast Event
detection
Fast
1 Event
buffer
Mapping RAM

## Slide 15
Fast Event – Fast Event Low Priority Mode
Return to normal mode after processing Fast Event
Micro-Research Finland Oy
RX
DC FIFO
Fast Event
detection
1 Event
buffer
Mapping RAM

## Slide 16
Fast Event – Example with FIFO depth of 5 events
Micro-Research Finland Oy
Received Event | Normal Mode | Fast Event High Priority | Fast Event Low Priority
0x00 | 0x00 | 0x00 | 0x00
0x01 | 0x00 | 0x00 | 0x00
0x02 | 0x00 | 0x00 | 0x00
0x03 | 0x00 | 0x00 | 0x00
0x04 | 0x00 | 0x00 | 0x00
0x05 | 0x00 | 0x00 | 0x00
0x00 | 0x01 | 0x01 | 0x01
0x00 | 0x02 | 0x02 | 0x02
0x00 | 0x03 | 0x03 | 0x03
0xFE | 0x04 | 0xFE | 0x04
0x00 | 0x05 | 0x04 | 0x05
0x00 | 0x00 | 0x05 | 0xFE
0x00 | 0x00 | 0x00 | 0x00
0x00 | 0x00 | 0x00 | 0x00
0x00 | 0xFE | 0x00 | 0x00
0x00 | 0x00 | 0x00 | 0x00
0x00 | 0x00 | 0x00 | 0x00

## Slide 17
Fast Event – Example with FIFO depth of 5 events (dropped events)
Micro-Research Finland Oy
Received Event | Normal Mode | Fast Event High Priority | Fast Event Low Priority
0x00 | 0x00 | 0x00 | 0x00
0x01 | 0x00 | 0x00 | 0x00
0x02 | 0x00 | 0x00 | 0x00
0x03 | 0x00 | 0x00 | 0x00
0x04 | 0x00 | 0x00 | 0x00
0x05 | 0x00 | 0x00 | 0x00
0x00 | 0x01 | 0x01 | 0x01
0x00 | 0x02 | 0x02 | 0x02
0x00 | 0x03 | 0x03 | 0x03
0xFE | 0x04 | 0xFE | 0x04
0xFE | 0x05 | 0xFE | 0x05
0x00 | 0x00 | 0x05 | 0xFE
0x00 | 0x00 | 0x00 | 0x00
0x00 | 0x00 | 0x00 | 0x00
0x00 | 0xFE | 0x00 | 0x00
0x00 | 0xFE | 0x00 | 0x00
0x00 | 0x00 | 0x00 | 0x00